## Slide 1: Hydrology signature in superconducting gravimeter readings
Jiaxin Liu
Philipp Schollmeier
February 7th, 2023, Stuttgart

## Slide 2: Measurement site
Fig. 1: Location of the BFO (Google Maps)
Black Forest Observatory near the village of Schiltach
Notes: -In a remote location with few human sources of noise
-Granite bedrock -> less movement of ground with changing pressure

## Slide 3: Measurement site
Fig. 2: Layout of the BFO (own picture)
SG in an old silver and cobalt mine
About 100 m under the surface
Notes: -BFO is at the edge of a valley with a small creek, SG about 500 m inside mountain
-Stable temperature of around 8°C inside, air locks provide fairly stable pressure
-Not included in graphic are soil moisture probes

## Slide 4: Mesurement site
Fig. 48: Soil moisture probes at the BFO

## Slide 5: Measurement site
Fig. 3: Tunnel of the mine (own picture)
Notes: - One of the cables connect SG and outside pressure sensor

## Slide 6: Data
All data are from 2022
Two sensors of the superconducting gravimeters SG056 – G1-F60 and G2-F60, vertical offset of 20 cm between them
Fig. 4: Overview of available data
Notes: - RELATIVE measurements of gravity!

## Slide 7: Workflow

## Slide 8: Data
Fig. 5: Uncalibrated gravity measurements of both sensors
Notes: Outliers at G1-F60 in September
Different magnitudes of voltage

## Slide 9: Calibration

## Slide 10: Calibration
Fig. 6: Calibrated measurements of both sensors
Given calibration coefficients for both sensors

## Slide 11: Calibration
Fig. 6: Calibrated measurements on April 8th

## Slide 12: Corrections
Measurements consist of multiple signals
We are interested in
are big outliers in data, can be caused by operators working on the instrument, will be eliminated
has causes in GIA, slow earthquakes or tectonics; is ignored
Summands 2, 3, 4 and 5 will be subtracted

## Slide 13: Corrections

## Slide 14: Removing outliers
Fig. 7: Differences between two sensors before outlier filtering

## Slide 15: Removing outliers
Fig. 8: Removing outliers

## Slide 16: Removing outliers
Fig. 9: Comparison of gravity series before and after outlier removal

## Slide 17: Tides

## Slide 18: Tides
Fig. 10: Synthetic tides
Notes: - Pole tide: Chandler period (400 days)

## Slide 19: Tides
Fig. 11: Tide subtraction

## Slide 20: Tides
Fig. 12: Tide subtraction on Apr 8th

## Slide 21: Atmospheric pressure

## Slide 22: Atmospheric pressure
Fig. 13: Outside pressure series over the year
Notes: - Data gaps because of interrupted connection between SG and pressure gauge after a storm

## Slide 23: Atmospheric pressure
Fig. 14: Density scatter plot between inside and outside pressure

## Slide 24: Atmospheric pressure
Fig. 15: Pressure series at the hut

## Slide 25: Atmospheric pressure
Fig. 17: Density scatter plot between outside
pressure and gravity residuals
Notes: - Mention correlation coefficient

## Slide 26: Atmospheric pressure
Fig. 18: Density scatter plot between inside
pressure and gravity residuals
Notes: - Mention correlation coefficient

## Slide 27: Atmospheric pressure
Fig. 19: Gravity residuals after pressure correction, gaps filled
by inside pressure

## Slide 28: Atmospheric pressure
Fig. 21: Gravity residuals on April 8th before and after atmospheric correction

## Slide 29: Atmospheric factor

## Slide 30: Atmospheric factor
Fig. 22: Density scatter plot between outside pressure and gravity residuals of sensor 1, without drift correction

## Slide 31: Atmospheric factor
Fig. 23: Density scatter plot between outside pressure and gravity residuals of sensor 2, without drift correction

## Slide 32: Atmospheric factor
Fig. 24: Density scatter plot between outside pressure and gravity residuals of sensor 2, with drift correction

## Slide 33: Atmospheric factor
Fig. 25: Density scatter plot between outside pressure and gravity residuals of sensor 2, with drift correction

## Slide 34: Remaining frequencies

## Slide 35: Remaining frequencies
Fig. 26: Gravity residuals of both sensors in April after removing atmospheric influence
Notes: Frequencies with small amplitudes, especially tidal, are still visible
Load tides are not removed perfectly, parameters were estimated for a longer period

## Slide 36: Remaining frequencies
Lunar day = 0.966 cpd, half lunar day = 1.933 cpd
Fig. 27: Lomb-scargle analysis of gravity series of sensor 1, biggest peaks marked

## Slide 37: Remaining frequencies
Observation model:
Where include the amplitudes of the oscillations, the gravity residuals
are the eliminated frequencies
An unweighted linear adjustment is carried out to estimate the amplitudes

## Slide 38: Remaining frequencies
Eliminated frequencies: 1 day, 1 lunar day, ½ day, ½ lunar day
Fig. 28: Gravity series before and after frequency elimination

## Slide 39: Remaining frequencies
Fig. 29: Fitted Oscillations in April

## Slide 40: Additional slides - Remaining frequ.
Fig. 30: Comparison of gravity series before and after frequency elimination

## Slide 41: Remaining frequencies
Fig. 31: Comparison of PSDs before and after frequency elimination

## Slide 42: Removing drift

## Slide 43: Removing drift
Fig. 32: Gravity series before and after removing drift

## Slide 44: Differences between sensors
Fig. 33: Differences between sensors after all corrections

## Slide 45: Differences between sensors
Fig. 34: Comparison between the differences and original readings of sensor 1

## Slide 46: Differences between sensors
Amplitude of differences: 0.1 Gal
Amplitude of original series: 220 Gal
Value of calibration coefficient for sensor 1 should be reduced by 0.0182 Gal/V
should be calculated more accurately with a full adjustment

## Slide 47: Hydrology

## Slide 48: Mesurement site
Fig. 48: Soil moisture probes at the BFO

## Slide 49: Hydrology
Fig. 35: Recorded soil moisture over the year (Solidus 1, probe 0)
Includes many outliers -> filtering, linear interpolation

## Slide 50: Hydrology
Fig. 36: Soil moisture series after outlier removal (Solidus 1, Probe 0)

## Slide 51: Hydrology
Fig. 37: soil moisture and gravity on April 8th
Significant raining event on April 8th
Gravity trend as expected, but there are also other factors involved

## Slide 52: Hydrology
Fig. 38: Comparison of soil moisture (Solidus 1, both probes) and gravity over the month of April

## Slide 53: Hydrology
Fig. 39: Comparison of soil moisture (Solidus 1, both probes) and gravity over the year

## Slide 54: Hydrology
Fig. 40: Scatter plot of soil mositure and gravity residuals

## Slide 55: Hydrology
Fig. 41: results after fitting a scale

## Slide 56: Hydrology
Fig. 42: Precipitation in mm/hour

## Slide 57: GRACE

## Slide 58: GRACE
GRACE Follow-On data up to degree 96 without filtering from ICGEM
Monthly solution only up to October
Adding of degree 1 coefficients and replacing C2,0 and C3,0 from the GRACE Technical Notes #13 and #14 of the NASA GRACE documentation

## Slide 59: GRACE
Fig. 43: Radius = 1000 km (above); Radius = 600 km (bottom) almost no change

## Slide 60: GRACE
Fig. 44: = 96 (above) ; = 10 (bottom) The error increases with increasing Grad

## Slide 61: GRACE
Fig. 45: with love number (above) ; without love number (middle) difference (bottom)

## Slide 62: GRACE
Fig. 46: Comparison of gravity residuals from SG(daily mean) and GRACE/GRACE FO

## Slide 63: GRACE
Fig. 47: Comparison of gravity residuals, GRACE, soil mositure and precipitation over full year

## Slide 64: Outlook
Comparing GRACE data and gravity over longer time period, perhaps with daily GRACE solutions
Try to explain remaining timeseries:
  inner Earth gravity model
  Find a good model that connects SM and gravity residuals
  Investigate remaining frequencies

## Slide 65: References
Neumeyer, Barthelmes, Dierks, et al. Combination of temporal gravity variations resulting from superconducting gravimeter (SG) recordings, GRACE satellite observations and global hydrology models. J Geodesy 79, 573–585 (2006). https://doi.org/10.1007/s00190-005-0014-8

## Slide 66: Additional slides - Atmospheric press.
Fig.16: Pressure series at the hut after filtering

## Slide 67: Additional slides – Remaining frequ.
Fig. 27: Lomb-scargle analysis of gravity series of sensor 2

## Slide 68: Additional slides – Remaining frequ.
Fig. 28: Full Lomb-scargle analysis for sensor 1

## Slide 69: Additional slides - Remaining frequ.
Fig. 28: Full Lomb-scargle analysis for sensor 1
Notes: - Inverse Depiction!!!

## Slide 70: Additional slides - Remaining frequ.
Eliminated frequencies: 354 days, 1 day, 1 lunar day, ½ day, ½ lunar day
Fig. 29: Gravity series before and after frequency elimination

## Slide 71: Additional slides - Remaining frequ.
Fig. 31: Comparison of gravity series before and after frequency elimination

## Slide 72: Additional slides – differences between sensors
Fig.: differences between sensors with new calibration coefficient